Welded Connections

Calculation complies with SNiP II-23-81*

General Properties

Steel: C345  категория 3

| Importance factor | 1 |
| --- | --- |
| Service Factor | 1 |
| Group of structures according to table 50* SNiP II-23-81* | 1 |

| Properties of welding materials |
| --- |
| Characteristic strength of weld metal based on the ultimate strength, Rwun | 490 N/mm2 |
| Design shear strength of fillet welds, Rwf | 215 N/mm2 |
| Welding type | Automatic and semiautomatic, diameter of the electrode wire not less than 1.4-2.0 mm |
| Position of weld | Flat |
| Climatic region | with temperature t > -40°C |

| Type | Properties |
| --- | --- |
|  | tf = 6 mm Leg of weld near flange = 4 mm Leg of weld near web = 4 mm |

Results of analysis by load case combinations

|  | N | My | Qz | Mz | Qy |
| --- | --- | --- | --- | --- | --- |
|  | kN | kN*m | kN | kN*m | kN |
| 1 | 0 | 75 | 0 | 0 | 0 |

| Checked according to SNiP | Check | Utilization Factor |
| --- | --- | --- |
| Sec. 11.2 Formula (120) | Of the weld metal | 0,951 |
| Sec. 11.2 Formula (121) | Of the metal of the fusion border | 0,796 |

Utilization Factor 0,951 - Of the weld metal

Utilization factor over whole package of combinations 0,951 - Of the weld metal

Interaction Curves

| Fixed values of forces | Qz = 0 kN Mz = 0 kN*m Qy = 0 kN |
| --- | --- |
| Range of forces | -918,765 kN < N < 919,512 kN -78,898 kN*m < My < 78,898 kN*m |

Interaction Curves

| Fixed values of forces | My = 0 kN*m Mz = 0 kN*m Qy = 0 kN |
| --- | --- |
| Range of forces | -918,795 kN < N < 919,512 kN -371,768 kN < Qz < 371,768 kN |

Interaction Curves

| Fixed values of forces | My = 0 kN*m Qz = 0 kN Qy = 0 kN |
| --- | --- |
| Range of forces | -918,635 kN < N < 919,512 kN -16,817 kN*m < Mz < 16,817 kN*m |

Interaction Curves

| Fixed values of forces | My = 0 kN*m Qz = 0 kN Mz = 0 kN*m |
| --- | --- |
| Range of forces | -919,512 kN < N < 919,512 kN -548,477 kN < Qy < 548,477 kN |

Interaction Curves

| Fixed values of forces | N = 0 kN Mz = 0 kN*m Qy = 0 kN |
| --- | --- |
| Range of forces | -78,958 kN*m < My < 78,958 kN*m -371,518 kN < Qz < 371,518 kN |

Interaction Curves

| Fixed values of forces | N = 0 kN Qz = 0 kN Qy = 0 kN |
| --- | --- |
| Range of forces | -78,903 kN*m < My < 78,903 kN*m -16,815 kN*m < Mz < 16,815 kN*m |

Interaction Curves

| Fixed values of forces | N = 0 kN Qz = 0 kN Mz = 0 kN*m |
| --- | --- |
| Range of forces | -78,961 kN*m < My < 78,961 kN*m -547,986 kN < Qy < 547,986 kN |

Interaction Curves

| Fixed values of forces | N = 0 kN My = 0 kN*m Qy = 0 kN |
| --- | --- |
| Range of forces | -371,478 kN < Qz < 371,52 kN -16,83 kN*m < Mz < 16,83 kN*m |

Interaction Curves

| Fixed values of forces | N = 0 kN My = 0 kN*m Mz = 0 kN*m |
| --- | --- |
| Range of forces | -371,783 kN < Qz < 371,783 kN -547,894 kN < Qy < 547,894 kN |

Interaction Curves

| Fixed values of forces | N = 0 kN My = 0 kN*m Qz = 0 kN |
| --- | --- |
| Range of forces | -16,83 kN*m < Mz < 16,83 kN*m -547,857 kN < Qy < 547,857 kN |

Report created 2021.02.09 21:23:43 (UTC+02:00) by Kristall (64-bit), version: 21.1.9.9 dated 05.01.2021