Welded Connections

Calculation complies with SNiP II-23-81*

General Properties

Steel: C245

| Importance factor | 1 |
| --- | --- |
| Service Factor | 1 |
| Group of structures according to table 50* SNiP II-23-81* | 1 |

| Properties of welding materials |
| --- |
| Characteristic strength of weld metal based on the ultimate strength, Rwun | 490 N/mm2 |
| Design shear strength of fillet welds, Rwf | 215 N/mm2 |
| Welding type | Semiautomatic, with solid wire, diameter of the electrode wire less than 1.4 mm |
| Position of weld | Flat |
| Climatic region | with temperature t > -40°C |

| Type | Properties |
| --- | --- |
| Section - GOST Equal angle GOST 8509-93 L75x8 | b = 175 mm  = 51,71 degree t = 10 mm Free leg of fillet weld = 6 mm Connected leg of fillet weld = 6 mm |

Results of analysis by load case combinations

|  | N |
| --- | --- |
|  | kN |
| 1 | 425 |

| Checked according to SNiP | Check | Utilization Factor |
| --- | --- | --- |
| Sec. 11.2 Formula (120) | Of the weld metal | 1,018 |
| Sec. 11.2 Formula (121) | Of the metal of the fusion border | 0,921 |

Utilization Factor 1,018 - Of the weld metal

Utilization factor over whole package of combinations 1,018 - Of the weld metal

Interaction Curves

| Range of forces | -417,621 kN < N < 417,621 kN |
| --- | --- |

Report created 2021.02.05 20:23:28 (UTC+02:00) by Kristall (64-bit), version: 21.1.9.9 dated 05.01.2021