Welded Connections

Calculation complies with SNiP II-23-81*

General Properties

Steel: C235

| Importance factor | 1 |
| --- | --- |
| Service Factor | 1 |
| Group of structures according to table 50* SNiP II-23-81* | 4 |

| Properties of welding materials |
| --- |
| Characteristic strength of weld metal based on the ultimate strength, Rwun | 410 N/mm2 |
| Design shear strength of fillet welds, Rwf | 180 N/mm2 |
| Welding type | Manual |
| Position of weld | Flat |
| Climatic region | with temperature t > -40°C |

| Type | Properties |
| --- | --- |
|  | Weld leg = 10 mm b = 260 mm h = 60 mm t = 12 mm tf = 20 mm |

Results of analysis by load case combinations

|  | N | My | Qz |
| --- | --- | --- | --- |
|  | kN | kN*m | kN |
| 1 | 1380 | 0 | 0 |

| Checked according to SNiP | Check | Utilization Factor |
| --- | --- | --- |
| Sec. 11.2 Formula (120) | Of the weld metal | 0,944 |
| Sec. 11.2 Formula (121) | Of the metal of the fusion border | 0,734 |

Utilization Factor 0,944 - Of the weld metal

Utilization factor over whole package of combinations 0,944 - Of the weld metal

Interaction Curves

| Fixed values of forces | Qz = 0 kN |
| --- | --- |
| Range of forces | -1461,6 kN < N < 1461,6 kN -78,392 kN*m < My < 78,392 kN*m |

Interaction Curves

| Fixed values of forces | My = 0 kN*m |
| --- | --- |
| Range of forces | -1460,931 kN < N < 1461,6 kN -393,476 kN < Qz < 393,476 kN |

Interaction Curves

| Fixed values of forces | N = 0 kN |
| --- | --- |
| Range of forces | -78,369 kN*m < My < 78,38 kN*m -393,646 kN < Qz < 393,646 kN |

Report created 2021.02.05 20:51:54 (UTC+02:00) by Kristall (64-bit), version: 21.1.9.9 dated 05.01.2021