Welded Connections

Calculation complies with SNiP II-23-81*

General Properties

Steel: C285

| Importance factor | 1 |
| --- | --- |
| Service Factor | 1 |
| Group of structures according to table 50* SNiP II-23-81* | 1 |

| Properties of welding materials |
| --- |
| Characteristic strength of weld metal based on the ultimate strength, Rwun | 450 N/mm2 |
| Design shear strength of fillet welds, Rwf | 200 N/mm2 |
| Welding type | Manual |
| Position of weld | Flat |
| Climatic region | with temperature t > -40°C |

| Type | Properties |
| --- | --- |
| Section - GOST Equal angle GOST 8509-93 L80x7 | Weld leg = 8 mm b = 150 mm h = 200 mm t = 10 mm tf = 12 mm |

Results of analysis by load case combinations

|  | N | My | Qz |
| --- | --- | --- | --- |
|  | kN | T*m | kN |
| 1 | 540 | 0 | 0 |

| Checked according to SNiP | Check | Utilization Factor |
| --- | --- | --- |
| Sec. 11.2 Formula (120) | Of the weld metal | 0,964 |
| Sec. 11.2 Formula (121) | Of the metal of the fusion border | 0,789 |

Utilization Factor 0,964 - Of the weld metal

Utilization factor over whole package of combinations 0,964 - Of the weld metal

Interaction Curves

| Fixed values of forces | Qz = 0 kN |
| --- | --- |
| Range of forces | -559,706 kN < N < 560 kN -3,995 T*m < My < 3,995 T*m |

Interaction Curves

| Fixed values of forces | My = 0 T*m |
| --- | --- |
| Range of forces | -559,591 kN < N < 560 kN -238,373 kN < Qz < 238,373 kN |

Interaction Curves

| Fixed values of forces | N = 0 kN |
| --- | --- |
| Range of forces | -3,999 T*m < My < 3,999 T*m -238,188 kN < Qz < 238,188 kN |

Report created 2021.02.05 20:29:56 (UTC+02:00) by Kristall (64-bit), version: 21.1.9.9 dated 05.01.2021